# Assign Map Categories
## Description
This functor assigns a set of categories to a map. The functor also allows combination or replacement of the existing map categories with a given set of categories.
## Inputs
Name	Type	Description
Input Map	Map Type	The map that receives the new categories.
Input Categories	Categorization Type	Categorization set (classes) to be assigned to the input map.

## Optional Inputs
Name	Type	Description	Default Value
Combine Categories	Boolean Value Type	If true, the functor will combine the categories of the input map with the given category set. Otherwise, the categories in the input map will be replaced by the given category set.	False

## Output
Name	Type	Description
Output Map	Map Type	A copy of the input map with a new categorization.

## Group
Map Algebra
## Notes
When “Combine Categories” is set, the functor combines the category sets, one from the input port and other from the input map. The main one is that passed as a parameter, thus, if both have an identical name or value, the category from the map will be replaced with the new one.
## Internal Name
AssignMapCategories