# Select Transition Matrix
## Description
This container picks up a transition matrix from a series of matrices.
## Inputs
## Optional Inputs
Name	Type	Description	Default Value
Step	Positive Int	Current step or model iteration.	1

## Outputs
Name	Type	Description
Transition Matrix	Transition Matrix	Matrix of transition rates.

## Group
Stack
## Notes
This container allows the replacement of one transition matrix with another during a model execution. Any matrix inside this container will begin to be used by a simulation according to its matrix number identifier and will continue to be used until the model step reaches the number identifier of another matrix inside the same container.
Each transition matrix inside the “Select Transition Matrix” must be provided by a corresponding Number Transition Matrix.
## Internal Name
SelectTransitionMatrix