# Ports
A port is a typed connection point on a functor. Input ports receive data; output ports produce it. Every functor defines a fixed set of ports — their names, types, and whether they are required or optional — and data flows between functors by connecting an output port of one to an input port of another.
## Input Ports
### Required and optional inputs
Every input port is either required or optional:
- Required ports must always be supplied — either by connecting an output from another functor or by providing a constant value directly. A model cannot run if a required input is missing.
- Optional ports have a default value that is used automatically when the port is not connected and no constant is provided. The default is specific to each port and is shown in the functor's documentation.
### Nullable inputs
Some optional ports are also nullable — they explicitly accept the absence of a value as meaningful input. A nullable port whose default is already none can be left without a value intentionally by supplying the constant .none. This is distinct from simply omitting the port (which uses the default) because it explicitly signals that no value is being provided.
### Editable inputs
An editable port can receive a constant value typed directly into the GUI or written as a constant in an EGO Script call. Non-editable ports must be connected to an output from another functor; they cannot be supplied with a constant.
### Auto-bound inputs and outputs
Some ports are auto-bound — when the functor is placed inside a compatible container, the port automatically connects to the relevant internal port of that container without needing an explicit connection. Auto-binding applies to both input and output ports.
Auto-bound input ports connect automatically to an internal output of the enclosing container:
- step — on Step, all Load* and Save* file I/O functors, and all Select* functors. Auto-binds to the step internal output of the enclosing loop container (Repeat, For, For Each, For Each Category, For Each Region, While, Do While).
- workdir — on all Load* and Save* file I/O functors. Auto-binds to the workdir internal output of the enclosing Workdir container.
- regionManager — on Get All Regions Info, Get Region Info, Region, Region Manager Value, Regional Map, Regional Categorical Map, Regionalize Map, Regionalize Categorical Map, Merge Regional Maps, Merge Regional Categorical Maps. Auto-binds to the regionManager internal output of the enclosing Region Manager, Region, or For Each Region container.
- regionId — on Get Region Info, Region, Regional Map, Regional Categorical Map, Regionalize Map, Regionalize Categorical Map. Auto-binds to the regionId internal output of the enclosing Region container.
- tableManager — on Merge Sub Tables, Sub Table, Table Manager Value. Auto-binds to the tableManager internal output of the enclosing Table Manager container.
- currentIndividual — on Get Current Individual. Auto-binds to the currentIndividual internal output of the enclosing Genetic Algorithm Tool container.
Auto-bound output ports connect automatically to an internal input of the enclosing container:
- condition — on Set While Condition. Auto-binds to the condition internal input of the enclosing While or Do While container.
- fitness — on Set Fitness. Auto-binds to the fitness internal input of the enclosing Genetic Algorithm Tool container.
## Output Ports
A functor may produce one or more outputs. In EGO Script, outputs are bound to variables using the := operator (see Functor calls). When a functor produces multiple outputs and only some are needed, the underscore _ discards unwanted ones:
// Bind all outputs
{ areaTable = areas } := CalcAreas { source = landscape };
// Bind only the first output; discard the rest
result := SomeFunctor input1 input2;
// Discard first output; keep second
_ secondOutput := SomeFunctor input1 input2;
## Port Naming
Port names follow different conventions depending on context:
- In EGO Script, port names are written in camelCase with a lowercase first letter: cellType, resultIsSparse, nullValue. See Nominal syntax for how port names appear in functor calls.
- In the GUI, the same ports are displayed with spaces between words and all words capitalised: “Cell Type”, “Result Is Sparse”, “Null Value”.
The conversion between the two follows the same rules as alias and variable name conversion in EGO Script.
## Port Types
Every port has a type that determines what data it can carry. A port accepts data of its exact type or any type that can be automatically converted to it. See the type system documentation for the full list of types and their conversions.
Two special constants are available for any input port regardless of type (see Constants):
- .UNBOUND — the port is not connected, or its connection is deliberately being ignored. Used especially when copying a fragment of a model to a text editor, where some connections may not be part of the selection.
- .none — the port is intentionally left without a value. Valid only for optional nullable input ports.
## Sequence Ports
Most container functors expose two special sequencing ports:
- sequenceInput — connecting a value here ensures the functor that produced that value completes before this container starts. Accepts any data type.
- sequenceOutput — pass this to another functor's sequenceInput to force this container to complete first.
These ports carry no data; their only purpose is to impose execution ordering. See Sequence ports in the EGO Script documentation for details and examples.
## Internal Ports (Container Functors)
Container functors communicate with the functors inside them through internal ports:
- Internal output ports carry values FROM the container INTO the contained functors. In EGO Script these are bound as the first declarations inside the container block using the { variable = portName } form.
- Internal input ports carry values FROM the contained functors BACK TO the container. These are set by dedicated functors placed inside the block (such as Set While Condition for the condition port of a loop).
### Internal outputs by container
Container	Internal output port	Type	Description
Do While	step	NonNegativeIntegerValue	Current iteration index, starting at 0.
For	step	RealValue	Current value in the numeric range being iterated.
For Each	step	RealValue	Current row value from the table being iterated.
For Each Category	step	IntegerValue	Current category code from the categorical map.
For Each Region	step	IntegerValue	Current region identifier.
For Each Region	regionManager	RegionManager	The region manager for the current region.
Repeat	step	NonNegativeIntegerValue	Current iteration index, starting at 0.
While	step	NonNegativeIntegerValue	Current iteration index, starting at 0.
Region Manager	regionManager	RegionManager	The region manager for the current region context.
Region	regionManager	RegionManager	The region manager.
Region	regionId	IntegerValue	The current region identifier.
Workdir	workdir	Workdir	The working directory defined by the container.
Table Manager	tableManager	TableManager	The table manager defined by the container.
Genetic Algorithm Tool	currentIndividual	LookupTableGroup	The current individual in the genetic algorithm population.

### Internal inputs by container
Container	Internal input port	Type	Set by
While	condition	BooleanValue	Set While Condition — the condition output port is auto-bound to this internal input.
Do While	condition	BooleanValue	Set While Condition — the condition output port is auto-bound to this internal input.
Genetic Algorithm Tool	fitness	RealValue	Set Fitness — the fitness output port is auto-bound to this internal input.

See Internal output ports and Internal input ports for EGO Script syntax details and examples.
## Hook Ports (Calculator Functors)
The five calculator functors (Calculate Map, Calculate Categorical Map, Calculate Value, Calculate Lookup Table Values, Calculate Lookup Table Keys And Values) connect their data inputs through hook functors rather than directly:
- Number Map ports — connect raster maps; referenced in expressions as i1, i2, …
- Number Table ports — connect tables and lookup tables; referenced as t1, t2, …
- Number Value ports — connect scalar values; referenced as v1, v2, …
In the abbreviated (shorthand) syntax, hook ports are implicit — operands are referenced directly by variable name using a type sigil (# for maps, % for tables, $ for values). See Calculator functor shorthand for details.